## Slide 1
RealTwin VISSIM Pipeline
How the network, MatchupTable, demand and turn routing are built | Oak Ridge National Laboratory

## Slide 2
Overview
What the pipeline does, and the one idea behind it

## Slide 3
What we are building
• A VISSIM version of the RealTwin SUMO workflow, driven over the Vissim COM API
• Inputs: a road network, turn counts from GridSmart cameras, signal timings from Synchro
• Output: a Vissim model loaded with traffic, ready to simulate
• Same method as the SUMO pipeline, so results can be compared simulator to simulator
• Built and tested against PTV Vissim 2026 on the Chattanooga corridor
Notes: The aim is parity: same inputs, same logic, same numbers. That is what lets a difference in results be attributed to the simulator rather than to the model build.

## Slide 4
The stages
# | Stage | Produces | State
1 | Import network | Vissim network + list of turn movements | Done
2 | MatchupTable | Sheet linking network, counts and signals | Done
3 | Vehicle inputs | Traffic entering the model | Done
4 | Turn routes | Which way traffic turns, and in what proportion | Done
5 | Signal control | Traffic signal timings | Not started
6 | Right turn on red | RTOR and stop control | Not started
Notes: Stages 1 to 4 are complete and checked against the SUMO pipeline on the same corridor.

## Slide 5
The words we use
• Link - a piece of road. Vissim splits a network into many short links
• Connector - a short stitch joining one link to the next (about 1.5 m here)
• Junction - an intersection. Vissim fills it with small internal links
• Approach - the link a vehicle arrives on at a junction
• Movement - one turn: from one approach to one exit. The unit of everything
• Bearing - the compass direction a piece of road points, in degrees
Notes: Chattanooga has 10 junctions, 34 approaches and 104 movements. Every later stage is expressed per movement.

## Slide 6
Step 1
How we find a junction

## Slide 7
The problem
• Vissim renumbers everything when it imports a network - old IDs are worthless
• It also turns every road into a link, including the little roads inside a junction
• So after import we have 441 links and no idea which belong to which intersection
• First attempt: read the junction out of the link's name
• That worked, but only because SUMO had written its own names into the file
• A network from RoadRunner, CARLA or a survey firm has no such names
Notes: The name-based method was a dead end for anyone not starting from SUMO. Worse, it would have failed silently and fallen back to guessing by distance.

## Slide 8
The fix: ask the OpenDRIVE file
• OpenDRIVE is the standard format the network is handed to Vissim in
• Every road in it carries a 'junction' tag: which junction it belongs to, or -1 for none
• Both that tag and the junction's ID are REQUIRED by the standard
• So every valid file has them, whoever produced it
• Vissim names each imported link after the road it came from, e.g. '473-0-Right'
• That road number is the bridge: file says road 473 is in junction 14
Notes: This is the key portability change. Chattanooga: 186 roads, 17 junctions, 127 roads inside one and 59 ordinary roads - which matches exactly what the old method found, from a completely different source.

## Slide 9
Checked: same answer, different route
What | From OpenDRIVE | From SUMO names (old)
Junction groups | 17 | 17
Same grouping of links | yes | -
Movements | 104 | 104
Junctions kept | 10 | 10
Turn mix | R28 T28 L26 U22 | identical
Notes: The two methods partition the links identically. Only the labels differ, because OpenDRIVE numbers junctions its own way.

## Slide 10
Two safeguards
• Not every group of roads is an intersection
  – A junction must have at least 3 approaches; below that it is a mid-block joint
  – Chattanooga: 17 groups found, 7 dropped, 10 real intersections
• Vissim builds its own 'segment node' per junction when it imports
  – We compare our list against those nodes and report any disagreement
  – The nodes cannot do the job themselves - they also cover the approaches
Notes: Node membership is 25 links at the largest junction against 17 internal ones, because a node is a polygon over the intersection and approaches poke into it. Useful as a check, not as the source.

## Slide 11
Step 2
Approaches, bearings and turns

## Slide 12
Bearing: which way a road points
• Every link is a line of points; a bearing is the compass angle between two of them
• 0 degrees is north, 90 east, going clockwise
• For an approach we use the LAST two points - the direction at the stop bar
• For an exit we use the FIRST two - the direction just after the turn
• The bits in between are ignored: connectors are ~1.5 m and internal roads curve
• Those curves are an artefact of how the junction was drawn, not of the manoeuvre
Notes: Measuring at the two ends nearest the junction gives a clean angle for the manoeuvre. Our bearings agree with SUMO's to a mean of 0.07 degrees, computed completely independently.

## Slide 13
Turn: comparing the two bearings
• Subtract the approach bearing from the exit bearing
• Change of 20 degrees or less -> straight ahead ('thru')
• Change of about 180 degrees -> U-turn
• Otherwise clockwise -> right, anticlockwise -> left
• Movements are then SORTED by that angle, sharpest right first
• That ordering matters more than it looks - see the next section
Notes: The 20 degree cut is the one judgement call, inherited from the SUMO side. It is worth revisiting on a network where it can be checked.

## Slide 14
Naming the approach: NB, EB, SB, WB
• NOT by absolute compass direction - that breaks on angled intersections
• Junction 8 has legs at 52 and 114 degrees: both are 'eastbound' by sector,
• and nothing is northbound, though the camera clearly counts northbound traffic
• Instead: sort the legs clockwise starting from north-west (337.5 degrees)
• Then the 1st leg takes the 1st direction the count file names, 2nd the 2nd, and so on
• Geometry decides the ORDER. The count file decides the NAMES
Notes: 337.5 is where a 45-degree sector centred on north begins, so a road pointing 350 degrees sorts first with the other northbound legs instead of last. The formula is taken from RealTwin's SUMO code so both tables sort the same way.

## Slide 15
Worked example: junction 9
Leg | Bearing | Sorted position | Named
link 22 | 111.5 deg | 1st | EB
link 17 | 235.1 deg | 2nd | SB
link 8 | 292.0 deg | 3rd | WB
Notes: The camera file for this intersection reports EB, SB and WB movements and no northbound ones, so those three names are handed out in order. Note link 17 points south-WEST but is called southbound - because that is what the camera operator called it.

## Slide 16
Step 3
Building the MatchupTable

## Slide 17
What the MatchupTable is
• One row per movement - one line for each turn at each junction
• It joins three separate worlds so they can refer to each other:
  – Network - which Vissim links the movement uses
  – Demand - which camera file, and which turn within it
  – Signal - which Synchro intersection, and which phase
• 104 rows for Chattanooga. It is the only file a person touches
Notes: Same purpose as the SUMO MatchupTable, and laid out so columns A to N sit in the same order, with one Vissim-only column parked at the end for the internal links a movement crosses.

## Slide 18
The movement code: NBL, NBT, EBR ...
• Code = direction + turn letter. R right, T through, L left, U U-turn
• So the left turn off the southbound leg is 'SBL'
• That string is the column heading in the camera's spreadsheet
• Match the code, read the count - that is the whole join
• Safety rule: down one approach the codes must run in order R, T, L, U
• because the movements were sorted by turning angle, so codes cannot jump about
Notes: The ordering rule is what catches a misclassified turn without needing anything to compare against.

## Slide 19
What a person supplies, and what is generated
Field | Who | Chattanooga
Which camera file for each junction | person | 6 cells
Which Synchro intersection ID | person | 6 cells
Which Synchro file | person | 1 cell
Intersection name and survey date | generated | auto
Turn code per movement, counts | generated | 80 rows
Turn code per movement, signals | generated | 80 rows
Notes: 13 cells out of 104 rows. Those 13 are field knowledge - which camera watches which intersection - and cannot be derived. RealTwin's SUMO flow asks for exactly the same 13.

## Slide 20
Corrections stay put
• Warnings point at rows worth checking; a person fixes them in the sheet
• Re-running the stage used to overwrite those fixes - the tool undid its own advice
• Now anything a person has entered is kept, and the run says what it would have changed
• --regenerate rebuilds from scratch, for after the derivation itself is fixed
• This matters: the SUMO MatchupTable itself has 11 hand-corrected cells
Notes: Running RealTwin's own generator over the committed SUMO table changes 11 cells, so that file is not purely generated either. Any pipeline of this kind needs a durable escape hatch.

## Slide 21
Step 4
How it lines up with the SUMO MatchupTable

## Slide 22
The two tables describe the same road, differently
• Same junctions, same approaches, same movements - independently derived
• But the ID numbers differ, because each tool numbers junctions its own way
• SUMO numbers them 2, 3, 4, 7, 8, 9, 10, 11, 12, 18
• OpenDRIVE numbers the same ten 2, 4, 5, 7, 9, 10, 11, 13, 14, 15
• We use the OpenDRIVE numbers, so the pipeline works on any file
• The translation is written to <name>_junctions.csv and used by nothing
Notes: Recording the mapping rather than depending on it. netconvert happens to write the SUMO junction ID into the OpenDRIVE junction's name field, which is where the translation comes from - but that field is optional in the standard, so the pipeline never reads it.

## Slide 23
The junction translation table
OpenDRIVE ID | SUMO ID | Internal links | Real intersection?
2 | 2 | 16 | yes
4 | 3 | 17 | yes
11 | 10 | 16 | yes
14 | 12 | 17 | yes
15 | 18 | 4 | yes
1 | J4 | 2 | no - mid-block
Notes: Written by stage 1 as <name>_junctions.csv. The seven 'J' entries are places SUMO created a node for a lane drop or name change, not intersections; they fail the three-approach test.

## Slide 24
Result: the two tables agree
What was compared | Result
Junctions | 10, same set
Approaches | 34, same per junction
Movements | 104, same per junction
Turn labels (left/thru/right/U) | 104 / 104
Count codes (NBL, EBR ...) | 104 / 104
Signal codes | 104 / 104
Approach code sets | 34 / 34
Bearings | mean difference 0.07 deg
Notes: Generated with no SUMO file open: 13 cells typed by hand, everything else from the Vissim network and the raw camera and Synchro files. The SUMO table was opened afterwards only to score the result.

## Slide 25
Step 5
Vehicle inputs - traffic entering the model

## Slide 26
What a vehicle input is
• The point where traffic enters the model, and how much
• Sits on an 'entry link' - a road at the edge of the network
• Carries a volume in vehicles per hour for each 15-minute period
• Camera counts come in 15-minute bins, so the model follows the real profile
• Chattanooga 07:00-09:00: 16 entry links, 8 periods, 7,499 vehicles
Notes: Periods with no data are written as zero rather than left blank, so a gap cannot silently inherit the previous period's volume.

## Slide 27
What counts as an entry link
• Nothing feeds into it - no connector arrives
• AND it leads somewhere - it feeds something
• The second half matters: the import leaves two disconnected stubs behind
• Traffic put on a stub could never reach the network
• Result: 16 entry links, exactly the 16 SUMO uses
Notes: SUMO's network has 18 links nothing feeds, but its flow file writes only 16 - it skips the same two stubs.

## Slide 28
Counts are measured at junctions; traffic enters at the edge
• So each counted approach is traced back upstream to the true entry
• This kept failing, leaving every count stranded at the junction it was measured at
• Cause: Vissim splits a junction into several internal links
• One road upstream then looks like several different roads arriving - a false merge
• Stepping over the internal links fixes it: 186 links resolve to 59 real roads
• SUMO's network also has 59. One entry link had been left with no traffic at all
Notes: This is the bug that left entry link 2 empty while overloading the two counted approaches downstream of it.

## Slide 29
Vehicle inputs against SUMO
What | SUMO | VISSIM
Entry links written | 16 | 16
Entry links carrying traffic | 12 | 12
Volume profiles matching exactly | - | 12 of 12
Vehicles, 07:00-09:00 | - | 7,499
Notes: Every entry link SUMO gives traffic to has a Vissim vehicle input with an identical 15-minute profile, to the vehicle. Before the fixes this was 9 of 12.

## Slide 30
Step 6
Turn routing

## Slide 31
What a routing decision is
• A marker on the road. A vehicle crossing it is given a route to follow
• Each route ends downstream and carries a share of the traffic
• Shares come straight from the camera counts, so the split matches reality
• Key rule: a vehicle already on a route IGNORES any further markers
• Chattanooga: 34 decisions, 104 routes, one per movement
Notes: That last rule drives the whole design. A marker placed where vehicles are still on an earlier route has its turn shares silently discarded.

## Slide 32
One decision per approach, covering every turn
• Not one decision per turn - that multiplies markers and risks them being ignored
• Turns with no count data get a route with share 0, not no route
• Why: a turn with no route is not 'unknown' to Vissim, it is forbidden
• A zero is visible, and becomes live the moment a number replaces it
• 346 of 832 route-shares are currently zero, at the four uncounted junctions
Notes: It also makes calibration easy: changing a turn percentage later is editing one number, not adding network objects and re-checking placement.

## Slide 33
Where the markers go
• A route must finish before the next marker starts, or that marker is ignored
• A marker only takes effect on the NEXT simulation step, so a gap is required
• That gap is calculated, not guessed: fastest vehicle in one step = 3.33 m
• Markers are pushed as far upstream as the rules allow, for maximum warning
• 7 of 34 moved back past their own approach, gaining 741 m of notice in total
Notes: Junction 4's marker gained 110 m, junction 2's gained 348 m. The walk only crosses a road where traffic cannot branch off, or vehicles not heading for the junction would be given a turn through it.

## Slide 34
A physical limit on short approaches
Link | Lanes | Length | Distance needed to cross lanes
47 | 5 | 12.98 m | 22.5 m - impossible
43 | 2 | 7.51 m | 7.5 m - exactly the length
38 | 3 | 24.96 m | 12.5 m - tight when busy
Notes: Vissim's own formula: 5 m of road per lane change plus a base distance. Link 47 is five lanes in thirteen metres. The simulation reported 56 warnings of vehicles failing to reach their turn.

## Slide 35
Combined routing - the remedy, optional
• Vissim can join a decision to the routes that end just before it
• A vehicle then learns at one junction which way it turns at the NEXT
• So it changes lanes across the intervening road instead of at the stop bar
• The manual describes this as preventing 'artificially causing queues'
• OFF by default, switched on with --combine-routes
• Because it changes how vehicles behave, not just what is in the file
Notes: This is the documented answer to the 45.8 m median approach against a 200 m lane-change distance. It is the modeller's call, so the pipeline never turns it on by itself. Verified: 34 of 34 decisions combined when asked, 0 when not.

## Slide 36
Checking the work
Especially where there is nothing to compare against

## Slide 37
Three real defects, all found by comparing with SUMO
• An upstream trace that never worked, leaving an entry link empty
• Two movements sharing one code, so a count was used twice
  – That inflated one approach by 60 percent - it looked like a plausible volume
• A code attached to the wrong movement while the totals still matched
• None would have crashed anything. A wrong model runs perfectly happily
Notes: This is why the comparison work was worth the effort. The failure mode here is silence, not error messages.

## Slide 38
But the next corridor has no SUMO table
• So the checks that matter are the ones needing nothing to compare against
• Codes down an approach must run R, T, L, U - a break means two turns clash
• Traffic leaving one junction should roughly equal traffic reaching the next
• Legs too close together to order confidently are reported
• A movement the camera reports but the road network lacks is reported
• Tested: the original faulty code triggers these on the real data, with no SUMO file
Notes: Two of the three historical defects would have been caught this way. The third, the empty entry link, would not - that gap is known and stated rather than papered over.

## Slide 39
Judging a warning
• Not everything flagged is broken - the message has to say which is which
• A U-turn the camera counts that the road cannot make: normal, just a note
• A right turn the camera counts that the network lacks: worth a look
• Traffic dropping between two junctions: probably driveways, possibly an error
• The tool reports and explains. A person decides
Notes: Chattanooga produces four notes about U-turns at three-leg junctions, two warnings about movements the network lacks, and one flow imbalance of -28 percent between junctions 8 and 10 - most likely the shopping mall entrances between them.

## Slide 40
Where we are

## Slide 41
Status
Stage | State | Evidence
Import network | Done | 104 movements, 10 junctions, any OpenDRIVE file
MatchupTable | Done | 104/104 against the SUMO table, generated standalone
Vehicle inputs | Done | 12/12 volume profiles match to the vehicle
Turn routing | Done | 34 decisions, 104 routes, placement rules verified
Combined routing | Done, optional | 34/34 when asked, off by default
Signal control | Not started | Format already understood (.prbc)
Right turn on red | Not started | Must be designed, not ported from SUMO
Notes: Everything through stage 4 is written into the Vissim model and reproducible from scripts.

## Slide 42
Three things worth carrying forward
• Nothing is trusted until checked - and how you compare matters
  – Matching row by row agreed while a code sat on the wrong movement
• The pipeline no longer depends on SUMO having produced the network
  – Junctions come from the OpenDRIVE standard, which any file has
• Right turn on red will NOT be a port of the SUMO logic
  – SUMO has no such concept; Vissim models it physically
Notes: The comparison lesson is the general one: an aggregate agreeing does not mean the parts agree.