## Slide 1
Building the MatchupTable
How SUMO does it, how the VISSIM pipeline does it, and why they agree

## Slide 2
What a MatchupTable is
• One row per movement - one line for each turn at each intersection
• It ties three separate worlds together so they can refer to each other:
  Network - which road or link the traffic comes from and goes to
  Demand - which camera file, and which turn within it
  Signal - which Synchro intersection, and which phase
• 104 rows for Chattanooga. It is the only file a person edits
• Both pipelines build one. Same purpose, same layout, different ID spaces
Notes: Everything downstream - vehicle inputs, routing, signal timings - is keyed on these rows. If a row is wrong, the model is wrong in a way that still runs.

## Slide 3
SUMO
How RealTwin builds it today

## Slide 4
SUMO does not classify turns - it reads them
• netconvert has already decided every turn and written it into the network
• Each <connection> carries a dir attribute: s, l, L, r, R or t
• RealTwin just translates those letters:
  s -> thru l, L -> left r, R -> right t -> Uturn
• So the turn labels come from SUMO's own geometry engine, not from RealTwin
• This matters: there is no threshold in RealTwin to get wrong
Notes: get_net_connections in rt_matchup_table_generation.py. The direction_mapping dictionary is the whole of RealTwin's turn logic on the SUMO side. L and R are 'partially left/right' in SUMO and fold into plain left/right.

## Slide 5
How the SUMO table is assembled
chatt.net.xml (the SUMO network)
  |
  +-- generate_junction_bearing()
  | approach bearings from the lane shapes
  | -> Junction ID, Degree, Approach Edge
  |
  +-- get_net_connections()
  | reads <connection from= to= dir=>
  | -> FromEdge, ToEdge, Turn
  |
  +-- format_junction_bearing()
  merges the two, renames the columns,
  strips the leading '-' from every edge id,
  sorts by junction, then bearing from 337.5 deg, then turn
  |
  v
MatchupTable.xlsx demand and signal columns BLANK
Notes: Bearings are measured from the last two shape points of the incoming lane. The 337.5 degree origin makes a road pointing just west of north sort first, so northbound legs are listed before eastbound.

## Slide 6
A trap in the column names
• The SUMO table's columns are called JunctionID_OpenDrive, FromRoadID_OpenDrive
• They do not contain OpenDRIVE IDs. They contain SUMO IDs
• format_junction_bearing simply renames the columns and strips a minus sign
  Junction ID -> JunctionID_OpenDrive FromEdge -> FromRoadID_OpenDrive
• Measured: the table's road ids run 280-3271, exactly SUMO's edge range
• The real OpenDRIVE road ids in the same network run 449-575. No overlap
Notes: RealTwin renames every SUMO edge to -<n> in parse_SUMO_ID, so stripping the minus sign is the whole conversion. The SUMO pipeline never leaves SUMO's ID space - netconvert is run, but nothing downstream reads OpenDRIVE ids back. The _OpenDrive suffix is vestigial.

## Slide 7
VISSIM
Why it has to start again, and how it does

## Slide 8
Why the Vissim side cannot reuse any of it
• Vissim renumbers the whole network when it imports OpenDRIVE
  OpenDRIVE roads 390-575 become Vissim links 1-186
• The SUMO table's ids are SUMO edge ids, so they never matched anyway
• And they are not durable: regenerating the .xodr with SUMO 1.24 instead of
  1.21 shifted every road id, with ZERO overlap with the committed table
• So the pipeline re-derives its own junctions, bearings and turns from Vissim
Notes: This is the central design decision. Everything else follows from it. The Vissim pipeline is standalone after the OpenDRIVE import.

## Slide 9
Finding junctions - by geometry, the default
• Every <road> in an OpenDRIVE file carries a junction attribute: an id, or -1
• Both that attribute and the junction's id are REQUIRED by the standard
• Each Vissim link is matched back to its OpenDRIVE road by its shape
  one link per drivable road, so it is a 1:1 assignment, not a nearest search
  cost combines shape, length and lane count; solved optimally
• The road's junction attribute then gives the junction. No link names read
Notes: Vissim does name each link after the OpenDRIVE road it came from, and --junction-source name uses that. But the naming convention is PTV's, not the standard's, so nothing guarantees it survives. Geometry was measured identical to the name route on every link of three networks: Chattanooga 186, a synthetic grid 84, an OSM extract 516.

## Slide 10
From links to movements
junction 15 -> interior Vissim links {101, 102, 103, 104}
APPROACHES - links feeding an interior link from OUTSIDE the group
  link 27 --conn--> 103 27 is outside -> approach
  link 41 --conn--> 101 41 is outside -> approach
  link 46 --conn--> 102 46 is outside -> approach
  101 --conn--> link 47 leaving -> exit, not an approach
FILTER - fewer than 3 approaches is a mid-block joint, not an intersection
  17 groups -> 10 real intersections
MOVEMENTS - walk each approach through the interior to every exit
  46 -> [102] -> 49 27 -> [103] -> 50
  27 -> [104] -> 49 41 -> [101] -> 47
34 approaches -> 104 movements
Notes: Chattanooga: 441 Vissim objects = 186 links + 255 connectors. Of the 186 links, 127 are junction-internal and 59 are ordinary roads.

## Slide 11
Turns - the same rule SUMO uses
• A turn cannot be classified from its own angle alone
• SUMO's NBNode::getDirection, which is what wrote those dir attributes:
  inside 44 deg -> straight, UNLESS another movement off the approach is straighter
  beyond 44 deg -> left or right U-turn is decided structurally
• We previously used a symmetric 20 deg cut, and it broke on two skewed approaches
  -21.3 and -28.4 deg were called left; SUMO calls both thru
• Porting the real rule took the movement table from 102/104 to 104/104
Notes: Both failures were on approaches where nothing was straighter, so SUMO's 44 degree band kept them as through movements while a 20 degree cut did not. A naive 'straightest wins' rule is worse, not better: it scores 100/104, because at a T-junction with no through movement it promotes a genuine 89 degree right turn to thru. The conjunction of both tests is what works.

## Slide 12
How the Vissim table is assembled
chatt.net.xml -> netconvert -> chatt.xodr -> Vissim COM import
  |
  +-- match each Vissim link to its OpenDRIVE road by geometry
  | -> the road's junction attribute gives the junction
  |
  +-- approaches from the connectors, filtered at 3 legs
  |
  +-- bearings from the Vissim link polylines
  | approach: last two points exit: first two points
  |
  +-- turns by SUMO's rule, per approach
  |
  +-- sorted by junction, bearing from 337.5 deg, then turn
  |
  v
MatchupTable.xlsx demand and signal columns BLANK
Notes: Deliberately the same sort order as the SUMO table so the two can be read side by side. Columns A-N are positionally identical; a Vissim-only column recording the junction-internal links a movement crosses is parked at the end.

## Slide 13
The hand input
The part no file can tell you

## Slide 14
13 cells, and they are the same 13 in both pipelines
• Three things cannot be derived from any network file - they are field knowledge:
  File_GridSmart which camera file watches this junction
  IntersectionID_Synchro which Synchro INTID is this junction
  File_Synchro the one UTDF file for the whole network
• Chattanooga: 13 cells out of 104 rows. Everything else is derived from them
• The intersection name, the date, and all 80 turn codes come for free
Notes: RealTwin's SUMO flow asks for exactly the same 13. This is not a Vissim limitation - it is the irreducible human input. Six of Chattanooga's ten junctions carry a camera file; the other four are minor nodes and are left blank in both tables.

## Slide 15
Typing them, or copying them
• Normally you type those 13 cells. That is the real workflow, in both pipelines
• --seed-from is a TESTING shortcut on the Vissim side only:
  it copies the 13 cells out of an already-filled SUMO MatchupTable
  so the two tables can be compared without re-typing anything
• RealTwin's SUMO flow has no equivalent - there is no other table to copy from
• In a standalone Vissim run there is no --seed-from at all
Notes: This is why the junction coordinates matter more than the seeding does. For a new corridor there is nothing to copy from, so the artefact that helps is junction_locations.csv: every junction with its latitude, longitude and a map link, so you can see which intersection you are filling in.

## Slide 16
Copying needs the junction mapping
• The two tables number junctions differently, and the numbers overlap misleadingly
  OpenDRIVE 2 is SUMO 2, but OpenDRIVE 10 is SUMO 8, and 11 is SUMO 10
• Matching by the bare number handed junction 10 the wrong intersection's counts
  it got Shallowford & Napier, a 4-leg intersection; it is the 3-leg I-75 ramp
• The only symptom was a warning about 3 approaches against 4 reported directions
• Fixed: seeds now translate through the mapping stage 1 records
Notes: The mapping was already being written to <name>_junctions.csv - stage 2 simply never read it. netconvert writes the SUMO junction id into the OpenDRIVE junction's name attribute, which is where the translation comes from. Seeding went from 3 junctions to 6, and derived codes from 32 to 80.

## Slide 17
The two methods side by side
 | SUMO | VISSIM (default)
Junctions from | SUMO net.xml junctions | OpenDRIVE <road junction>
Links matched by | n/a - stays in SUMO | geometry, 1:1 assignment
Bearings from | lane shape, last 2 points | link polyline, last 2 points
Turns from | netconvert's dir attribute | same rule, ported
ID space | SUMO edge / junction ids | OpenDRIVE road / junction ids
Hand input | 13 cells | 13 cells
Turn codes derived | positionally | per row, from its own bearing
Notes: The one real difference is the ID space, which is why the junction mapping exists as an artefact.

## Slide 18
They agree
• Junctions 10 = 10
• Approaches 34 = 34
• Movements 104 = 104
• Turn labels 104 / 104 identical
• Turn mix thru 30, right 28, left 24, Uturn 22 on both sides
• Junction mapping confirmed by coordinates - worst separation 1.98 m
Notes: The mapping was checked geometrically as well as by id: for all ten junctions the mapped SUMO junction is the nearest one, and the runner-up is between 9 and 686 times further away. The camera file assignment also transfers 10 of 10, with the same four junctions deliberately blank in both.

## Slide 19
What to open and check
File | What it holds
datasets/example1/updated_net/MatchupTable_updated.xlsx | the SUMO table, in SUMO ids
vissim/work/chattanooga/MatchupTable.xlsx | the Vissim table, in OpenDRIVE ids
vissim/work/chattanooga/junction_mapping.csv | OpenDRIVE <-> SUMO ids, coordinates, Vissim links
vissim/work/chattanooga/movement_mapping.csv | all 104 movements, both tables side by side
vissim/work/chattanooga/junction_locations.csv | each junction's latitude, longitude and map link
Notes: junction_locations.csv is the one that matters for a new corridor: it needs no SUMO network at all.